# OV SINGLE BASKET STRAINER

## Model OV

(Sizes 20mm (3/4”) – 150mm (6”)

OV Single basket strainers provide a cost-effective

method of protecting pipeline equipment, cleaning

liquids or salvaging valuable solids. Incorporated

are a number of special features and optional extras.

The filter is of cast construction and is supplied with

one high quality stainless steel cylindrical basket.

It is used in liquid handling installations where the

flow can be shut off for short periods to allow the

removal of the basket for cleaning.

## MAIN FEATURES

- High quality 316 grade stainless steel basket with large filtration areas resulting in low pressure drops.

- Compact design for space saving.

- Working pressures up to 50 barg (A300 Series).

- Quick release filter covers and knobs for easy maintenance.

## OPTIONS

- Range of extras allowing filter to be customised.

- Available in cast iron, cast steel, bronze or stainless steel.

- Visual/Electrical differential pressure indicators are available.

- Magnetic columns (pre-magnetic filtration).

Product Details.

| MODEL | OV | OV/S | OV/GM | OV/SS |
| --- | --- | --- | --- | --- |
| Body Material | Cast Iron BS EN1561/EN-JL1030 | Cast steel BS EN10213-2/1.0625 | Cast Gunmetal BS1400 GRD LG4C | Cast Stainless Steel BS 1504 316 C16 |
| Cover Material | Cast Iron BS EN1561/EN-JL1030 | Cast steel BS EN10213-2/1.0625 | Cast Gunmetal BS 1400 GRD LG4C | Stainless Steel BS 1504 316 C16 |
| Maximum working pressure | 17 barg at 50(C | 22 barg at 50(C. A300 Series = 50 barg at 50(C | 22 barg at 50(C (3/4”-1½” = 13.8 barg) | 22 barg at 50(C A300 Series = 48 barg at 50(C |
| Basket | Stainless Steel Basket and Mesh Lining BS1449 Grade 316 S31 |
| Drain plug | Brass | Stainless Steel | Gunmetal | Stainless Steel |
| Vent | Stainless Steel | Stainless Steel | Phosphor Bronze | Stainless Steel |
| Standard seals | Nitrile (-30(C to +120(C) | Nitrile (-30(C to +120(C) | Nitrile (-30(C to +120(C) | Viton (-20(C to +200(C) |
| Body colour | Blue | Silver | Self | Self |

Dimensions and weights.

SCREWED BSPP OR NPT (Dimensions in mm)

| N.B (A) | B | C | D | E | F | G | H | J | K | L | Basket Area | Weight |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ¾” (20mm) | 159 | 108 | 103 | 220 | 73 | 105 | 64 | 50 | 86 | ½” BSP | 184cm2 | 5kg |
| 1” (25mm) | 159 | 108 | 103 | 220 | 73 | 105 | 64 | 50 | 86 | ½” BSP | 184cm2 | 5kg |
| 1¼” (32mm) | 174 | 108 | 129 | 306 | 73 | 145 | 90 | 50 | 122 | ½” BSP | 268cm2 | 7kg |
| 1½” (40mm) | 174 | 108 | 129 | 306 | 73 | 145 | 90 | 50 | 122 | ½” BSP | 268cm2 | 7kg |
| 2” (50mm) | 270 | 156 | 165 | 351 | 112 | 156 | 112 | 76 | 131 | ½” BSP | 484cm2 | 19kg |
| 2½” (65mm) | 270 | 156 | 165 | 351 | 112 | 156 | 112 | 76 | 131 | ½” BSP | 484cm2 | 19kg |

Note: Weights based on cast iron units.

FLANGED (Dimensions in mm)

| N.B (A) | B | C | D | E | F | G | H | J | K | L | M | N | Basket Area | Weight |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1” (25mm) | 194 | 108 | 103 | 220 | 73 | 105 | 64 | 50 | 86 | ½” BSP | 124 | 16 | 184cm2 | 8kg |
| 1¼ (32mm) | 210 | 108 | 129 | 306 | 73 | 145 | 90 | 50 | 122 | ½” BSP | 156 | 18 | 268cm2 | 12kg |
| 1½” (40mm) | 210 | 108 | 129 | 306 | 73 | 145 | 90 | 50 | 122 | ½” BSP | 156 | 18 | 268cm2 | 12kg |
| 2” (50mm) | 310 | 156 | 165 | 351 | 112 | 156 | 112 | 76 | 131 | ½” BSP | 165 | 20 | 484cm2 | 25kg |
| 2½” (65mm) | 310 | 156 | 165 | 351 | 112 | 156 | 112 | 76 | 131 | ½” BSP | 191 | 22 | 484cm2 | 25kg |
| 3” (80mm) | 343 | 175 | 198 | 451 | 132 | 210 | 140 | 76 | 186 | ½” BSP | 210 | 22/24 | 718cm2 | 42kg |
| 4” (100mm) | 356 | 175 | 234 | 575 | 132 | 265 | 175 | 76 | 241 | ½” BSP | 229/254 | 24 | 964cm2 | 45kg |
| 6” (150mm) | 480 | - | 296 | 728 | 160 | 361 | 218 | - | 330 | ½” BSP | 318 | 26 | 1835cm2 | 100kg |

Dimensions left of the oblique are for cast iron filters, Dimensions right of the oblique are for steel, stainless steel and gunmetal.

Note: Weights based on cast iron units.

Please note:

- These specifications refer to standard products only. Alternative materials for bodies (e.g. monel, hastalloy) and seals (e.g. EPDM, PTFE) are available on request.

- Higher pressure filters are available up to 50 barg.

- Working pressure is stated at 50°C. to verify suitability of this equipment above this temperature or below 0°C, please contact our technical sales desk.

- Whilst alternative seal materials e.g. EPDM, PTFE are available and can be used to offer a wide range of chemical compatibility and working temperatures up to 260°C, it is recommended that such applications are discussed with our technical sales desk.

Revision status – Revision01, March 2007.

Our policy is one of continuous improvement and we reserve the right to alter any details of our products at any time without prior notice.