# OW DUAL BASKET STRAINER

Model OW

(Sizes 20mm (3/4”) - 200mm (8”)

For applications where the requirement is for

continuous flow with minimum loss of pressure,

the dual filter provides quality of design and

performance.

The filter is of cast construction and incorporates

two chambers each containing a high quality

stainless steel basket.  Flow is diverted from one

chamber to the other without interruption by turning

the handle, which rotates dual cylindrical cocks.

MAIN FEATURES

- Simple changeover operation requires infrequent maintenance.

- Compact design.

- Large filtration areas giving low-pressure drops.

- Working pressures up to 50 barg (A300 Series).

- Quick release filter covers and knobs for easy maintenance.

- No contamination between filtered and unfiltered liquids.

- Wide range of materials, sizes and accessories.

- Filtration down to 10 microns.

- Handle covers chamber in use - preventing accidental opening of pressurized chamber.

- Differential pressure indicators as optional extras.

Product Details.

| MODEL | OW/O | OW/WB | OW/S | OW/S/WB | OW/C | OW/GM | OW/SS |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Body & Cover material | Cast Iron BS EN1561/EN-JL 1030 | Cast Iron BS EN1561/EN-JL 1030 | Cast Steel BS EN10213-2/1.0625 | Cast Steel BS EN10213-2/1.0625 | Cast Iron BS EN1561/EN-JL 1030 | Gunmetal BS 1400 GRD LG4C | Stainless Steel BS1504 Grade 316 C16 |
| Sleeve | Not Applicable | Bronze BS1400 LG2C | Not Applicable | Bronze BS1400 LG2C | Not Applicable | Not Applicable | Not Applicable |
| Change-over Cocks | SG Iron BSEN1563/EN-JS1020 | Bronze BS1400 LG2C | SG Iron BSEN1563/EN-JS1020 | Bronze BS1400 LG2C | Stainless Steel BS1504 Grade 316 C16 (Ni/PTFE coated) | Bronze BS1400 LG4C | Stainless Steel BS1504 Grade 316 C16 (Ni/PTFE coated) |
| Internal Machine Parts | Mild Steel BS970 230 M07 | Stainless Steel BS970 308 S31 | Mild Steel BS970 230 M07 | Stainless Steel BS970 308 S31 | Stainless Steel BS970 308 S31 | Phosphor Bronze BS1400 Grade PBI | Stainless Steel BS970 308 S31 |
| Baskets | Stainless Steel Basket and mesh lining BS1449 Grade316 S31 |
| Drain Plugs | Brass | Brass | Mild Steel | Brass | Stainless Steel | Phosphor Bronze | Stainless Steel |
| Vent | Steel | Brass | Steel | Brass | Steel | Brass | Brass |
| Seals | Nitrile (-30(C to + 120(C) | Nitrile (-30(C to + 120(C) | Nitrile (-30(C to + 120(C) | Nitrile (-30(C to + 120(C) | Nitrile (-30(C to + 120(C) | Nitrile (-30(C to + 120(C) | Viton (-20(C to + 200(C) |
| Maximum Working Pressure | 17 Barg at 50(C | 17 Barg at 50(C | 22 Barg at 50(C A300 Series = 50 Barg at 50(C | 22 Barg at 50(C A300 Series = 50 Barg at 50(C | 17 Barg at 50(C | 17 Barg at 50(C (3/4”-11/2” = 13.8 Barg) | 22 Barg at 50(C A300 Series = 48 Barg at 50(C |
| Body Colour | Red | Blue | Silver | Silver | Red | Self | Self |

# Dimensions and weights.

# SCREWED BSPP OR NPT (Dimensions in mm)

| A | B | C | D | E | F | G | H | J | K | L | M | N | Basket Area ea | Weight |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| ¾” (20mm) | 120 | 282 | 149 | 220 | 73 | 105 | 64 | 205 | 103 | 86 | 170 | ½” BSP | 184cm2 | 13kg |
| 1” (25mm) | 120 | 282 | 149 | 220 | 73 | 105 | 64 | 205 | 103 | 86 | 170 | ½” BSP | 184cm2 | 13kg |
| 1 ¼” (32mm) | 137 | 295 | 175 | 306 | 73 | 145 | 90 | 205 | 132 | 122 | 184 | ½” BSP | 268cm2 | 19kg |
| 1 ½” (40mm) | 137 | 295 | 175 | 306 | 73 | 145 | 90 | 205 | 132 | 122 | 184 | ½” BSP | 268cm2 | 19kg |
| 2” (50mm) | 184 | 425 | 216 | 351 | 112 | 156 | 112 | 219 | 165 | 131 | 280 | ½” BSP | 484cm2 | 49kg |
| 2 ½” (65mm) | 184 | 425 | 216 | 351 | 112 | 156 | 112 | 219 | 165 | 131 | 280 | ½” BSP | 484cm2 | 49kg |

Note: Weights based on cast iron units.

# FLANGED (Dimensions in mm)

| A | B | C | D | E | F | G | H | J | K | L | M | N | P | R | Basket Area ea | Weight |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1” (25mm) | 152 | 282 | 149 | 220 | 73 | 105 | 64 | 205 | 103 | 86 | 170 | ½” BSP | 124 | 16 | 184cm2 | 16kg |
| 1 ¼” (32mm) | 175 | 295 | 175 | 306 | 73 | 145 | 90 | 205 | 132 | 122 | 184 | ½” BSP | 156 | 18 | 268cm2 | 22kg |
| 1 ½” (40mm) | 175 | 295 | 175 | 306 | 73 | 145 | 90 | 205 | 132 | 122 | 184 | ½” BSP | 156 | 18 | 268cm2 | 22kg |
| 2” (50mm) | 210 | 425 | 212 | 351 | 112 | 156 | 112 | 219 | 165 | 131 | 280 | ½” BSP | 165 | 20 | 484cm2 | 52kg |
| 2 ½” (65mm) | 230 | 425 | 212 | 351 | 112 | 156 | 112 | 219 | 165 | 131 | 280 | ½” BSP | 191 | 20 | 484cm2 | 53kg |
| 3” (80mm) | 267 | 490 | 256 | 451 | 132 | 210 | 140 | 250 | 198 | 186 | 330 | ½” BSP | 210 | 22 | 718cm2 | 85kg |
| 4” (100mm) | 318 | 540 | 294 | 575 | 132 | 265 | 175 | 250 | 233 | 241 | 380 | ½” BSP | 254 | 24 | 964cm2 | 125kg |
| 6” (100mm) | 380 | 760 | 398 | 868 | 160 | 410 | 275 | 380 | - | 359 | 530 | ½” BSP | 318 | 25 | 2065cm2 | 250kg |
| 8” (200mm) | 570 | 1020 | 550 | 1210 | 248 | 520 | 390 | 500 | - | 472 | 700 | ½” BSP | 381 | 30 | 3980cm2 | 730kg |

Note: Weights based on cast iron units.

Please note: 6” unit also available as multi basket strainer – see insert drawing for dimensions.

Multi basket strainer - dimensions and weights.

(All dimensions in mm)

| A | B | C | D | E | F | G | H | J | Basket Area per chamber | Weight |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 6” (150mm) | 320 | 944 | 472 | 268 | 230 | 286 | 575 | 596 | 2065 cm2 | 250kg |

Note: Weight based on cast iron unit.

Please note:

- These specifications refer to standard products only. Alternative materials for bodies (e.g. monel, hastalloy) and seals (e.g. EPDM, PTFE) are available on request.

- Higher pressure filters are available up to 50 barg.

- Working pressure is stated at 50°C, to verify suitability of this equipment above this temperature or below 0°C, please contact our technical sales desk.

- Whilst alternative seal materials e.g. EPDM, PTFE are available and can be used to offer a wide range of chemical compatibility and working temperatures up to 260°C, it is recommended that such applications are discussed with our technical sales desk.

Revision status – Revision01, March 2007.

Our policy is one of continuous improvement and we reserve the right to alter any details of our products at any time without prior notice.